Reed Solomon codes are a subset of BCH codes and are linear block codes. A Reed-Solomon code is specified as RS(n,k) with s-bit symbols.

This means that the encoder takes k data symbols of s bits each and adds parity symbols to make an n symbol codeword. There are n-k parity symbols of s bits each. A Reed-Solomon decoder can correct up to t symbols that contain errors in a codeword, where 2t = n-k.

The following diagram shows a typical Reed-Solomon codeword (this is known as a Systematic code because the data is left unchanged and the parity symbols are appended):

Example: A popular Reed-Solomon code is RS(255,223) with 8-bit symbols. Each codeword contains 255 code word bytes, of which 223 bytes are data and 32 bytes are parity. For this code:

n = 255, k = 223, s = 8

2t = 32, t = 16

The decoder can correct any 16-symbol errors in the code word: i.e. errors up to 16 bytes anywhere in the codeword can be automatically corrected.

Given a symbol size s, the maximum codeword length (n) for a Reed-Solomon code is n = 2s – 1

For example, the maximum length of a code with 8-bit symbols (s=8) is 255 bytes.

Generator Polynomial

A Reed-Solomon codeword is generated using a special polynomial. All valid code words are exactly divisible by the generator polynomial. The general form of the generator polynomial is:

and the codeword is constructed using:

c(x) = g(x).i(x)

where g(x) is the generator polynomial, i(x) is the information block, c(x) is a valid codeword and is referred to as a primitive element of the field.

Example: Generator for RS(255,249)

# Code for Encoding  (by Simon Rockcliff)

register int i,j ;

int feedback ;

for (i=0;i<nn-kk;i++)  bb[i] = 0;

for (i=kk-1; i>=0; i--)

{  feedback = index_of[data[i]^bb[nn-kk-1]] ;

if (feedback != -1)

{ for (j=nn-kk-1; j>0; j--)

if (gg[j] != -1)

bb[j] = bb[j-1]^alpha_to[(gg[j]+feedback)%nn] ;

else

bb[j] = bb[j-1] ;

bb[0] = alpha_to[(gg[0]+feedback)%nn] ;

}

else

{ for (j=nn-kk-1; j>0; j--)

bb[j] = bb[j-1] ;

bb[0] = 0 ;

} ;

} ;

} ;